## Slide 1
KX-NS Step by Step Guide Activation Key
July 28, 2014
Specifications are subject to change without notice.
Panasonic System Networks PBX SE team
Notes: 1

## Slide 2
1. Activation Key List
Activation key for KX-TDE/NCP cannot be used for KX-NS PBX, even for same purpose.
Recording time expansion : 2h to 15h Automatic recording by supervisor Message backup to USB memory or NAS As “TVM204” : 2-ch based (*2) [2-way Record] button for PT or CA
*1)
As “Memory” to expand extension capacity to more than 30. This AK is only for KX-NS1000.
As “CO card” & “Extension Card” (same as TDE/NCP) Panasonic KX-UT phone is treated as Panasonic KX-NT IP-PT for activation key. (Not as SIP phone )
PBX to PBX one-look network for master and slave PBX See (*1).
To upgrade built-in UM to KX-TVM full features
Activation key is required for CTI server except CA and CSTA MUX. (same purpose as TDE/NCP)
(same purpose as TDE/NCP)
Enhance feature activation key for TDE/NCP is divided to Mobile feature and Enhanced QSIG feature.
(*2) Transfer Fax or VM using e-mail (server) / Built-in IMAP feature / Send fax (fax driver)
Notes: 2

## Slide 3
2. Conditions for One-look Network
- When virtual card is installed to slave PBX, these AK are required to slave PBX for quantity of ch. - Each maser and slave PBXs need each one AK. - Only maser PBX needs one AK because TIE table is programmed only in master PBX.
- When built-in VM(UM) of slave unit is used, these AK are required to slave unit. - Same as “Mobile Extension” and “CA”. - Only maser PBX needs one AK because master PBX communicates with CTI server.
- Only master PBX needs AK for quantity of “users in master PBX” and “users in slave PBXs”. - Only master PBX needs one AK.
Notes: 3

## Slide 4
Chapter 1 Activation Key Installation

## Slide 5
11. Window for Activation Key
Click “Activation Key”.
Notes: 5

## Slide 6
12. MPR ID
Confirm MPR-ID and get activation key file for the MPR-ID from Key Management System.
Notes: 6

## Slide 7
13. Activation Key File Installation
Install the activation key file.
Notes: 7

## Slide 8
14. Quantity of User
These features have to be enabled for extension. And activation key is required for quantity of user who want to enable these features.
- Extension / Cellular phone parallel ring (Keep ring after Fwd No Answer) - Virtual PS (Cellular) in ICD group - Remote walking COS through DISA without PIN - Automatic DISA connection for Fwd / Transfer to detect end of call for CO-CO
Mailbox based (Not Ext based)
Notes: 8

## Slide 9
Chapter 2 Temporary Activation Key
Notes: 9

## Slide 10
21. Temporary Activation Key
Expiration | 60-day | 180-day | 10-day
Built-in | Yes | No Download from KMS. KMS = Key Management System web | 
AK Type | Limited AK (See next page.) | Any AK | Any AK
PBX | KX-NS PBX only | KX-TDE/NCP/NS | KX-TDE/NCP/NS
Purpose | Trial If user likes the feature, sell regular AK. 60-day trial can start anytime for each feature. | Pay Later When dealer installs PBX hardware and inventory of AK is not enough, dealer can get this AK now and has to buy regular AK in 180-day. | Demo (and so on) When sales company or dealer wants to do demo, this AK is useful.
Remark | Trial is available only one-time for each one feature. | Download is available only one-time for one MPR card. | Download is available repeatedly. (8 times)
Temporary AK has 3 types.
Notes: .

## Slide 11
22. Built-in Temporary AK for Trial
Notes: .

## Slide 12
When 10-day AK or 180-day temporal AK is expired, system restarts automatically at midnight. You can view and delete temporal AK file manually before expiration.
23. After Expire
Notes: .

## Slide 13
Thank you !
Notes: 13

## Slide 14
Revision
Date | No. | Change
Sep 11 | - | First edition
Dec 14 | - | Picture was revised.
Mar 14 | 21 (Page 10) | 10-day activation key : 8 times
July 28 | 1 (Page 2) | KX-TVP full features => KX-TVM full features
Notes: 14